## Slide 1
Introduction to Quantum Computing
www.meetiqm.com
A lecture series by IQM and HS RM
Authors: Stefan Seegerer, Mikio Nakahara, Nikolay Tcholtchev
Last Updated 06/2025

## Slide 2: Why think about different computing paradigms?

## Slide 3: Sorting a list of numbers
8
2
5
3

## Slide 4: Sorting a list of numbers
2
8
5
3

## Slide 5: Sorting a list of numbers
2
3
5
8

## Slide 6
Thinking about new computing paradigms can lead to more efficient solutions

## Slide 8: There are problems, a classical computer cannot (efficiently) solve
Problem with current computers:
Intractable problems
Fundamental limits
Time & power limits
“Latest findings suggest global computing is more likely responsible for between 2.1% and 3.9% of greenhouse gas emissions.“
Current approach is not scalable!
https://www.upi.com/Science_News/2021/09/10/communications-tech-carbon-emissions/8771631295350/

## Slide 9: There are problems, a classical computer cannot (efficiently) solve
Graphics: ETH Zurich, Microsoft, ACM

## Slide 10: Overview
Computational complexity depends on the resource to implement the algorithm.
Different physical systems may be employed for information processing. Choosing a different one sometimes gives a different computational complexity than digital information processing.
Quantum information processing and quantum computation employ quantum systems to store and process information, which may reduce computational complexity for some tasks.

## Slide 11: Information is Physical. (R Landauer (IBM), 1991)
Physics laws can be used for information processing/computation.
Example: Evaluate the complete elliptic integral of the first kind
. .
Use physics. The period of a pendulum is
It may take a few minutes to set up a pendulum. It is much shorter than the time required to build a digital computer from scratch.
A physical system may be used as a computational resource. Its usage is limited in general though.

## Slide 12: Complexity depends on the device for processing
Complexity depends on a system to implement an algorithm.
There are some problems whose complexity may be reduced if they are implemented with complex vectors and matrices acting on them.
And quantum physics, the physics of the microscopic world, is described by complex vectors and matrices. Let’s use this system to execute such algorithms!

## Slide 13: Quantum Information Processing
Thanks to the progress of nanotechnology, it is now possible to fabricate a nanoscopic system that follows the laws of quantum mechanics. Superconducting qubits (=quantum bit) employed in IQM quantum computers are an example of such devices.

## Slide 14: Another Motivation for Quantum Computing
Moore’s law: The number of transistors that can be packed into a CPU is expected to double every two years.
As transistors shrink, we are rapidly approaching the atomic scale, where classical physics breaks down and quantum effects become dominant.
These quantum effects, rather than being an obstacle, offer a new way to process information, leading to quantum computing.
CC-BY 4.0 by Max Roser, Hannah Ritchie

## Slide 15: Bits and Qubits

## Slide 16: Classical Computer vs. Quantum Computer
Quantum bit
Classical bit
2 distinct states
0
1
0
1
switch on/off
State can be measured repeatedly
Superposition of 2 basis states
Point on the surface of a sphere
Measurement of the state will cause it to fall back to 0 and 1, no repeated measurement

## Slide 17: What is quantum computing?
Quantum computers follow different rules than classical computers – those of quantum physics.
Classical computer vs. Quantum computer
A bit can be either 0 or 1, while a qubit can be in a superposition: qubit can be both 0 and 1 at the same time.
Measurement will yield either 0 or 1.
Bit vs. Qubit (quantum bit)
0
1
0
1
Two qubits can be entangled. Changing one directly impacts the other.
→ 1 qubit can be in a superposition of 2 basis states → A 1 bit state can be just one out them
1Qubit
Basis states:
0
1

## Slide 18: What is quantum computing?
→ 2 qubits can be in a superposition of all 4 basis states → A 2-bit state can be just one out them
Quantum computers follow different rules than classical computers – those of quantum physics.
Classical computer vs. Quantum computer
A bit can be either 0 or 1, while a qubit can be in a superposition: qubit can be both 0 and 1 at the same time.
Measurement will yield either 0 or 1.
Bit vs. Qubit (quantum bit)
0
1
0
1
Two qubits can be entangled. Changing one directly impacts the other.
2 Qubits
1Qubit
2 Qubits
2 x basis states
Basis states:
00
01
10
11

## Slide 19: What is quantum computing?
Quantum computers follow different rules than classical computers – those of quantum physics.
Classical computer vs. Quantum computer
A bit can be either 0 or 1, while a qubit can be in a superposition: qubit can be both 0 and 1 at the same time.
Measurement will yield either 0 or 1.
Bit vs. Qubit (quantum bit)
0
1
0
1
Two qubits can be entangled. Changing one directly impacts the other.
3Qubits
2 Qubits
3Qubits
1Qubit
2 Qubits
3Qubits
2 x basis states
2 x basis states
Basis states:
000
100
010
110
001
101
011
111
000 001 010 011 100 101 110 111
3 qubits can be in a superposition of all 23 = 8 basis states
A 3-bit state can be just one of them

## Slide 20: What is quantum computing?
Quantum computers follow different rules than classical computers – those of quantum physics.
Classical computer vs. Quantum computer
A bit can be either 0 or 1, while a qubit can be in a superposition: qubit can be both 0 and 1 at the same time.
Measurement will yield either 0 or 1.
Bit vs. Qubit (quantum bit)
0
1
0
1
Two qubits can be entangled. Changing one directly impacts the other.
50 Qubits
50 Qubits
3Qubits
300 Qubits
50 Qubits
2 Qubits
3Qubits
1Qubit
50 Qubits
2 Qubits
3Qubits
2 x basis states
2 x basis states
250 states
Classical supercomputers hit a roadblock at 50 qubits (Technology Review)
300 Qubits
300 Qubits
300 Qubits
51 Qubits
000 001 010 011 100 101 110 111
3 qubits can be in a superposition of all 23 = 8 basis states
A 3-bit state can be just one of them

## Slide 21: What is quantum computing?
Quantum computers follow different rules than classical computers – those of quantum physics.
Classical computer vs. Quantum computer
A bit can be either 0 or 1, while a qubit can be in a superposition: qubit can be both 0 and 1 at the same time.
Measurement will yield either 0 or 1.
Bit vs. Qubit (quantum bit)
0
1
0
1
Two qubits can be entangled. Changing one directly impacts the other.
50 Qubits
300 Qubits
50 Qubits
3Qubits
300 Qubits
50 Qubits
2 Qubits
3Qubits
300 Qubits
1Qubit
50 Qubits
2 Qubits
3Qubits
300 Qubits
2 x basis states
2 x basis states
250 states
2300 states
Classical supercomputers hit a roadblock at 50 qubits (Technology Review)
Exponential increase in computational capacity
Enables new algorithms and solutions to previously intractable problems
000 001 010 011 100 101 110 111
3 qubits can be in a superposition of all 23 = 8 basis states
A 3-bit state can be just one of them

## Slide 22: “Quantum Parallelism”
Bit is replaced by qubit in quantum computing.
qubits represent up to different states
simultaneously.
1 | 2
10 | 1,024
20 | 1,048,576
30 | 1,073,741,824
40 | 1,099,511,627,776
50 | 1,125,899,906,842,624
60 | 
70 | 
80 | 
90 | 
100 | 
1,000 | 
1 | 2
10 | 1,024
20 | 1,048,576
30 | 1,073,741,824
40 | 1,099,511,627,776
50 | 
60 | 
70 | 
80 | 
90 | 
100 | 
1,000 | 
Eddington number . The number of atoms in the visible universe.
1,099,511,627,776
1,073,741,824

## Slide 23: Computational Complexity

## Slide 24: A suitable measure for complexity
In general, the effort required in terms of memory or time can be determined
Time is often the limiting factor
Sliced apple (space)
Apple compote (space)
Sliced apple (time)
Apple compote (time)
1 apples
3 apples
1 min
3 min
2 min
2 min

## Slide 25: A suitable measure for complexity
In general, the effort required in terms of memory or time can be determined
Time is often the limiting factor
The complexity is specified depending on the input size, but independently of the specific hardware
The O notation O(…) is widely used
  O(
In most cases, it is not the exact effort that is relevant, but the order of magnitude
Sliced apple (space)
Apple compote (space)
Sliced apple (time)
Apple compote (time)
1 apple
3 apples
1 min
3 min
2 min
2 min

## Slide 26: Complexity of algorithms
Notation | Type | Example
O(1) | constant | Add an item to the end of a list
O(n) | Linear | Finding an item in an unsorted list
O(nc) | Polynomial | Bubble Sort
O(cn) | Exponential | Traveling Salesman Problem, using dynamic programming
O(n!) | Factorial | Traveling Salesman Problem, using brute force

## Slide 27: Complexity of algorithms
Assuming one Million Instructions per second (MIPS)
The power of one Motorola 68000 (current processors have 100 000 MIPS)
 | n | n² | 2n | n!
n=10 | < 1s | < 1s | < 1s | 4s
n=30 | < 1s | < 1s | 18 m | 1025y
n=50 | < 1s | < 1s | 36 y | Very long
n=100 | < 1s | < 1s | 1017 y | Very long
n=1000 | < 1s | 1s | Very long | Very long
n=10000 | < 1s | 2 m | Very long | Very long
n=100000 | < 1s | 3 h | Very long | Very long
n=1000000 | 1s | 12 d | Very long | Very long
Notes: 1 MIPS (Motorola 68000 from 1979)
90.000 MIPS (i9-10900K)

## Slide 28: Computational Complexity
P: Solved in polynomial time.
NP: Verified in polynomial time.
NP-complete: Most difficult in NP.
NP-hard: At least as difficult as NP-complete. (Find the best solution among the NP-complete solutions, for example.)
BQP (Bounded error, Quantum, Polynomial time): Solvable in polynomial time by a quantum computer.

## Slide 29: Caution: Not All Algorithms Can Be Improved
A physical system cannot be an all-purpose computer (pendulum/spaghetti).
A quantum computer makes use of wave nature of quantum states. There are interference, superposition and entanglement associated with this. They do not exist in a classical (i.e., digital) computer.
Typical quantum algorithm; Grover’s database search, Shor’s factorization. They require a full-fledged quantum computer with built-in quantum error correction (QECC).
Currently available quantum computers, including the IQM quantum computer, are called the NISQ (Noisy Intermediate-Scale Quantum) computer. <1000 QB, no QECC. They are often used for the quantum-classical hybrid computation such as the Variational Quantum Eigensolver (VQE).

## Slide 30: Brief Summary of IQM Quantum Computer
10 mK

## Slide 31: Summary

## Slide 32: Summary
Physical system may be employed for information processing and computation.
Quantum computing employs the law of quantum physics to store, process and transfer information.
Thanks to the progress of nanotechnology, we can fabricate nanoscale devices that follow the law of quantum mechanics. Superconducting qubit in IQM quantum computer is an example of such systems.
Currently available quantum computer is called NISQ (Noisy Intermediate-Scale Quantum) computer. No QECC (N). <1000 qubits (IS).
We will see how quantum information processing is different from and superior to classical one in the following lectures.

## Slide 33: Practical notes

## Slide 34
CONFIDENTIAL
Outline of the course

## Slide 35: This course …
… is intended to be an introduction to the computing (not the physics aspects) of a quantum computer
… assumes you get actively engage with the lectures and the exercises
… uses qrisp as the SDK for developing quantum algorithms
… assumes access to quantum computers via IQM Resonance (freemium available) / IQM Server (on-prem users)
… is supported by the material and applets on IQM Academy

## Slide 36: qrisp
qrisp is a high level programming framework for working with quantum computing programs
It’s pythonic
It’s open source
https://github.com/eclipse-qrisp/Qrisp
qrisp.eu
pip install „qrisp[iqm]“

## Slide 37: Features of qrisp (you will learn about these throughout the course)
Typed quantum variables
Modularity
Compatibility and
interoperability
Works with IQM hardware
Arithmetics
automatic Uncomputation,
i.e. Garbage Collection

## Slide 38: There are different quantum computing frameworks, but qrisp will enable you to learn what matters

## Slide 39: IQM Resonance / IQM Server
A platform to run and organize your quantum circuits.
Made for education and research.
Support for multiple frameworks (qrisp, qiskit, Cirq and more)