## Slide 1
Error reduction
www.meetiqm.com
A lecture series by IQM
Authors: Alessio Calzona, Amin Hosseinkhani, Miha Papic, Pedro Figueroa-Romero, Manish Thapa, Raphael Amadeus Brieger & Stefan Seegerer
Last Updated 07/2025

## Slide 2: Real quantum hardware vs. simulator
Chart: 
| "00" | "01" | "10" | "11"
Expected | 0.502 | 0 | 0 | 0.498
Actual | 0.528 | 0.043 | 0.067 | 0.361
Noise is present in modern day quantum computers.
Until large scale error correction is reached, the algorithms of today must be able to remain functional in the presence of noise.
This makes strategies of reducing errors an important building block for creating quantum algorithms on today's quantum computers.
H
X
Notes: So far, our qpu simulator has been ideal.
Gates work exactly as defined by their unitary matrices and there are no ’noise’ in the circuit execution.
Running and measuring these gates will give us equal superposition in the simulator: 50/50 probability for the states
If we would run and measure this many times with real qpu, the probabilities wouldn’t be exactly 50/50 and even the the other basis states would be measured at times

## Slide 3: Incoherent Noise
Incoherent noise arises from the interaction of the quantum system with its environment, leading to a loss of quantum information (decoherence) and entanglement. These errors are stochastic and non-unitary, causing a quantum state to transition into a mixed state.
Energy Relaxation (T1): Loss of energy from the qubit to the environment, causing the qubit to decay from an excited state to its ground state.
Dephasing (T2): Loss of phase coherence due to environmental fluctuations, leading to a loss of the qubit's ability to interfere with itself.
Irreversible Process: Information lost due to incoherent noise cannot be fully recovered.
Clement Gódfrin, Quantum information processing using a molecular magnet single nuclear spin qudit, retrieved from ResearchGate

## Slide 4: Coherent Noise
Coherent noise refers to errors that are deterministic and unitary in nature, often arising from miscalibrations or imprecise control operations. Unlike incoherent noise, coherent errors preserve the purity of the quantum state and can, in principle, be reversed or compensated for.
Systematic Deviations: Constant offsets in control pulse amplitudes, phases, or frequencies.
Under/Over-Rotations: Gates applying slightly more or less than the intended rotation angle.
Controllable & Correctable: Unlike random incoherent noise, coherent errors arise from tunable aspects of our system. This opens the door for:
Precision Calibration: Dialing in control parameters for optimal performance.
Tailored Pulse Design: Engineering specific control sequences to cancel out systematic deviations.
https://www.iqmacademy.com/curriculum/assets/bloch-viz/index.html?gates=H,X,T,Y&noKet&noise
Try it yourself and apply the same operation (e.g. the X gate) multiple times.

## Slide 5
Some Potential Sources of Error in Superconducting Circuits
Energy Relaxation (T1)
Photon loss to environment through:
Dielectric loss in materials
Quasi-particle excitations
Radiative loss to control lines
Dephasing (T2)
Phase coherence loss due to:
Flux noise from trapped vortices
Charge fluctuations
Environmental temperature fluctuations
Leakage Errors
Population escaping computational subspace:
Excitation to |2⟩ states in transmons
Creates non-correctable, correlated errors
Persists across multiple gate operations
Crosstalk & Spectator Errors
Unwanted interactions from:
Dense wiring and control line coupling
Frequency collisions between qubits
Shared readout resonators

## Slide 6: How to fight noise?
Perform classical computations for
noise-aware compilation (e.g. qubit selection)
Correcting errors by post-processing classically
Hardware
Pulses
Applications/Circuits
Improving pulse signals
Optimal control
Compensating pulses
Improving hardware
chip design, shielding, …

## Slide 7: Modeling noise
Notes: Noise models help us predict how errors manifest and how they propagate through quantum circuits.

## Slide 8
Quantum Evolution
What we’ve covered so far:
Description of a quantum state:
The state evolves according to the Schrödinger equation:
The state after the evolution is therefore:
,
i.e. the matrix describes how an initial state evolves.
But what is the alternative?
Imagine a qubit interacting with some unknown environment, e.g.
The combined system (qubit + environment) still evolves according to the Schrödinger equation:
Works very well for an ISOLATED system!
Qubit ,
Environment ,
Interaction

## Slide 9
Quantum Evolution
In the real world the “environment” can be anything with the following properties:
- We do not have control over the environment (we cannot perform measurements etc.).
- We do not really care about the state of the environment; we are only interested in the qubit.
The dynamics of a qubit interacting with some environment = Open quantum system evolution!
Property | Isolated system | Open system
Quantum State |  | Statistical mixture of “pure” states!
Conservation of probability |  | , i.e. is positive semi-definite
Unitary time evolution, |  | 
Expectation value |  | 
Property | Isolated system | Open system
Quantum State |  | 
Conservation of probability |  | 
Expectation value |  | 

## Slide 10: State vector
describes closed quantum systems
Density matrix
can describe open quantum systems
Notes: The starting point of operation formalism is to generalise the state vector |𝜓>, we have used until now, to a density matrix 𝜌. State vectors describe only closed quantum systems, whereas density matrices can describe open quantum systems i.e. systems interacting with their environment.

## Slide 11: State vector
describes closed quantum systems
Density matrix
can describe open quantum systems
Notes: -The starting point of operation formalism is to generalise the state vector |𝜓>, we have used until now, to a density matrix 𝜌.
-State vectors describe only closed quantum systems, whereas density matrices can describe open quantum systems i.e. systems interacting with their environment.

## Slide 12: State vector
describes closed quantum systems
Density matrix
can describe open quantum systems

## Slide 13: State vector
describes closed quantum systems
Density matrix
can describe open quantum systems
amplitudes

## Slide 14: State vector
describes closed quantum systems
Density matrix
can describe open quantum systems
amplitudes
Superposition of and

## Slide 15: State vector
describes closed quantum systems
Density matrix
can describe open quantum systems

## Slide 16: State vector
describes closed quantum systems
Density matrix
Probabilities
can describe open quantum systems

## Slide 17: State vector
describes closed quantum systems
Density matrix
‘Coherences’
Probabilities
can describe open quantum systems

## Slide 18: State vector
describes closed quantum systems
Density matrix
‘Coherences’
Probabilities
Superposition of and
can describe open quantum systems

## Slide 19: State vector
describes closed quantum systems
Density matrix
‘Coherences’
Probabilities
Classical mixed state of and
can describe open quantum systems

## Slide 20: State vector
describes closed quantum systems
Density matrix
‘Coherences’
Probabilities
Classical mixed state of and
where gives the probability for the system being in state
can describe open quantum systems

## Slide 21
X
X
Describing noiseless quantum computers
[
Tensor product of unitary matrices of X gates

## Slide 22
X
X
Describing noiseless quantum computers

## Slide 23
X
X
Density matrix corresponding to
Describing noiseless quantum computers

## Slide 24
X
X
Density matrix corresponding to
Describing noiseless quantum computers

## Slide 25
X
X
Density matrix corresponding to
Describing noiseless quantum computers

## Slide 26
Density matrix corresponding to
X
X
Tensor product of unitary matrices of X gates
Tensor product of unitary matrices of X gates
Describing noiseless quantum computers

## Slide 27
Density matrix corresponding to
X
X
)
Describing noiseless quantum computers

## Slide 28
Density matrix corresponding to
X
X
Describing noiseless quantum computers

## Slide 29
Quantum Evolution
What are the properties of ?
A valid description of the time evolution must map a valid quantum state to a valid quantum state!
If then for any valid , ⇒ is TRACE-PRESERVING (TP)
If is positive semi-definite then is positive semi-definite ⇒ is POSITIVE (P)
Dynamical map
Turns out that POSITIVITY is not strict enough! …but why?
Assume we have:
  an initial state ,
  a dynamical map , acting on a part of the whole Hilbert space (e.g. one qubit in a quantum computer)
For the total evolution to be a valid physical map, must therefore be POSITIVE!
We will refer to this property as COMPLETE POSITIVITY!
A valid physical map is therefore COMPLETELY POSITIVE and TRACE-PRESERVING (CPTP)

## Slide 30
Kraus representation of dynamical maps
Any valid open quantum system evolution is described by a CPTP map.
But what does such a map look like?
Choi-Kraus theorem: A linear map is completely positive if and only if it admits a Kraus representation.
Trace-preservation

## Slide 31
Example 1: Amplitude damping channel
Each CPTP quantum evolution is described by a set of Kraus operators
The amplitude damping channel models the decay of an excitation into a thermalized environment
Kraus operators:
Does not affect the -state
Decreases the population of the -state
Transfers the population from to
This channel is TP:
The amplitude damping channel induces decays from the to the -state:

## Slide 32
Coherence times
People often report coherence times when discussing QPU performance
Thus far we have characterized our channels based on the probability to apply an error ()
Consider amplitude damping:
          is the probability for a decay of state to state
          these decays are independent and uncorrelated ⇒ Poisson process
          the probability of no errors occurring in a time interval is determined by the decay time
          For any Poisson process, we can equate ⇒
T1 experiment
Prepare initial state
Let state evolve for time
Plot probability of measuring at different values of
Fit exponential decay to extract coherence time -
Assume noise is described by amplitude damping!
T1 measures the timescale of the decay of the diagonal elements!

## Slide 33
Example 2: Pure dephasing channel
Amplitude damping “kills” the off-diagonal elements of the DM
In experiment, we often observe processes which affect the off-diagonal elements, but not the diagonals
Kraus operators:
Does nothing
Destroy coherences
The pure dephasing channel decays the value of the coherences = off-diagonal elements:
=
The ”strength” of this channel is experimentally characterized by the pure dephasing time

## Slide 34
T2 experiment
Prepare initial state
Let state evolve for time
Plot probability of measuring at different values of
Fit exponential decay to extract coherence time -
But we cannot “turn off” amplitude damping (with a decay time of )!
If only pure dephasing is present:
Pure dephasing + Amplitude damping
T2 measures the timescale of the decay of the off-diagonal elements!

## Slide 35
Example 3: Measurement
The Kraus formalism enables us to model the effects of a projective measurement!
The ”environment” in this case is the measurement apparatus interacting with the qubit.
Kraus operators:
Projects onto
The system after measurement is in a statistical mixture of the two measurement eigenstates:
Projects onto

## Slide 36
Modelling circuit operations with errors
Notes: Modelling gates, measurements, initalization with errors

## Slide 37
Modelling Noisy Gates
X
X
Amplitude damping (T1)
Pure dephasing (T𝛗)
Noiseless evolution:
Noisy evolution:
Apply gate.
Apply noise channels.

## Slide 38
Modelling Noisy Circuits
Noiseless evolution
Noisy evolution
Append noise channel after each gate
Can be more demanding computationally than noiseless simulation!
H
H
CZ
CZ
CZ
H
H
H
H
CZ
CZ
H
H
T1
T1
T1
T1
Error
Error
We have implicitly assumed no time-correlations in this model!

## Slide 39: Error supression

## Slide 40: What is error suppression?
Error suppression encompass a very wide set of techniques aiming at reducing the amount errors happening during the execution of a desired algorithm.
Error suppression is therefore deeply connected to the hardware properties of the QPU in use and it’s intertwined with topic such as QPU calibration, error characterization and even noise-aware circuit transpilation.
Importantly, error suppression does not rely on heavy post-processing and does not come with (significant) runtime overhead. Often, suppression techniques are applied unbeknownst to the general user.
In this set of slides, we’ll focus on two error suppression techniques:
  Dynamical decoupling
  Pauli Twirling

## Slide 41: Dynamical Decoupling (DD)
2
DD is a quantum control technique.
Meaning, the goal is to drive the dynamics in a particular and targeted way.
It is typically known to kill coherent (covered in the next slides) and non-Markovian errors in qubits.
AWS Blog: https://aws.amazon.com/blogs/quantum-computing/suppressing-errors-with-dynamical-decoupling-using-pulse-control-on-amazon-braket/

## Slide 42: Dynamical Decoupling (DD)
2
DD is a quantum control technique.
Meaning, the goal is to drive the dynamics in a particular and targeted way.
It is typically known to kill coherent (covered in the next slides) and non-Markovian errors in qubits.
AWS Blog: https://aws.amazon.com/blogs/quantum-computing/suppressing-errors-with-dynamical-decoupling-using-pulse-control-on-amazon-braket/

## Slide 43: Single qubit case
2
Let’s artificially add delay in the middle using IQM Pulla.
Check capacity of each sequence to preserve state.
Let us apply some gates, and do the inversion.
Ideally this operation should do nothing! But due to
errors, this is not the case.

## Slide 44: DD with IQM Quantum Computers
2
These are measurements performed at one of our internal stations.
Depending on the calibration set and error profile on a given day, DD offers error suppression to varying degrees.
DD is seen to significantly boost the performance, and especially so when the idles are long.
Delay experiment performed on one of the qubits
IRB of single qubit idling gate of different durations with and without DD sequences

## Slide 45: Pauli twirling (randomized compiling)
8
GOAL
To tailor coherent errors into a stochastic noise channel
HOW
By combining the results of many logically equivalent circuits (where random gates are locally added)
In the next slides, we cover:
  What are coherent errors?
  How to randomize a given circuit in practice?
  What do we gain from the randomization?

## Slide 46: Reminder: coherent errors
8
A coherent error is a unitary error with noise map
Can be small extra over/underrotations, spurious couplings, ...
Can not be completely removed (e.g., via better calibration)
Effects of coherent errors accumulate quadratically fasters than stochastic errors!
At the same time: average gate fidelity is insensitive to coherent errors:

## Slide 47: Simple example: single-qubit X overrotation
8
Let’s consider a single-qubit noise map associated with a small X rotation:
with, say, .
Let’s apply on a qubit initialized
in the state times and plot the probability
of measuring the qubit in the state.

## Slide 48: Simple example: single-qubit X overrotation
8
What if we randomly add pairs of (noiseless Z gates) before and after each ? (Twirled noise)
Z
Z
50% of the times:
50% of the times:
Adding pairs of Z gates does not change the noiseless circuit, as
However, when we sandwich the noisy map with Z, we flip the sign of the coherent X rotation.
By averaging over many (logically equivalent) randomized circuits, we get a much better result!

## Slide 49: How to do that in practice?
8
The example before is too simple for several reasons…
  The noise map always comes with a gate attached:
  There’s no such a thing as “noiseless gates” that one can add.
  What about coherent errors different from X over rotation?
but we can take care of those!
W can use and use the pair of twirling gates and
to twirl the noise map and still obtain a logically equivalent circuit!
Typically, single-qubit gates are an order of magnitude better than two-qubit gates. Use single qubit gates to twirl two qubit gates!
If the twirling gates are sampled form the Pauli group, all possible coherent errors are twirled into stochastic Pauli errors!

## Slide 50: How to do that in practice?
8
Example from arXiv:2010.00215
Original circuit
One instance of a randomized version of the original circuit, with random single-qubit Paulis (dashed black boxes) added before and after each CNOT layer
Exercise: verify that this circuit is logically equivalent to the original one!
The added random Paulis are compiled together with the existing single qubit gates into new single-qubit rotations (orange boxes)

## Slide 51: Effects of Pauli Twirling
8
arXiv: 2406.13967
Figure (a): Experimental noise of a CZ gate, visualized with error generator in the Pauli basis
Without Pauli twirling (a), there are many off-diagonal terms. Those indicate for example:
Non-unital errors (like T1 decay)
Coherent errors
Figure (b): With Pauli twirling the noise generator is approximately diagonal, showing that twirling successfully twirled the CZ noise into stochastic Pauli noise.

## Slide 52: Effects of Pauli Twirling
8
arXiv: 2406.13967
The noise generator is now much easier to measure and understand: 16 diagonal elements instead of 16x16 elements of the full matrix!
The average gate fidelity now gives a much more accurate picture, since it can only see the diagonal:

## Slide 53: Error mitigation

## Slide 54: What is error mitigation?
Unlike error suppression, error mitigation accepts the presence of errors during the execution of the desired algorithm and aims at mitigating their effects on the desired outcome.
This is typically done via (potentially heavy) post-processing, often combining together the outcomes of several non-logically equivalent circuits executed on the QPU.
In this sense, error mitigation is a second layer of error reduction which comes after the implementation of all possible error suppression techniques.
Successful error mitigation allows us to recover almost-error-free results even from very noisy circuits and it is therefore a key ingredient when running large and complicated algorithms before fully-fledged fault tolerant computers will be available.
The price to pay for “cancelling” large part of the noise is a significant sampling overhead, which scales exponentially in the noise level and circuit size. This means that, if the circuit is too noisy, the runtime required to execute the error mitigated algorithm explodes and becomes impractical. Typically, error mitigation is feasible when the number of expected detrimental errors per circuit run is up to .

## Slide 55: Types of error mitigation?
In the literature there are dozens of different proposed error mitigation techniques!
One simple (but sometimes too simplistic) approach to classify them is to distinguish them along three axes:
Targeted errors:
Requirements:
Accuracy:
Gate errors (happening in the bulk of the circuit)
Noise-agnostic (no noise characterization required)
“Bias-free” (provides noise-free results IF some assumptions are met)
Measurement errors (typically happening at the end of the circuit)
Noise-aware (precise noise characterization required)
Heuristic
(no accuracy guarantee but proved to work well in several scenarios)

## Slide 56: Readout error mitigation
We consider an approach that targets error happening in the final round of measurements
(mitigation of mid-circuit measurement is also possible but requires a slightly different approach)
The idea is to:
Define a simple (but often times effective) model for the noise process
Characterize the readout error rates for each qubit of the QPU (it’s a noise-aware technique!)
Use this information about readout noise to “undo” it in a post-processing stage.
At first, let cover these three important steps with a simple single-qubit example.

## Slide 57: Simple example: 1. Noise process
In general, measuring the state of a qubit is a complicated process where the qubit is coupled to a readout resonator and gradually collapse to one of the two computational states during the measurement time.
In practice, when it comes to readout errors, it turns out that it’s often enough to describe them in terms of classical bitflip probabilities. This means that:
With a probability a qubit is measured in even if it should have been measured in ;
With a probability a qubit is measured in even if it should have been measured in .
In general, those two probabilities are different and typically given the fact that an excited qubit is more likely to decade to its ground state during the measurement time.

## Slide 58: Simple example: 2. Noise charact.
The goal is to measure the two probabilities and .
To this end, we run two characterization circuits, each with shots:
In the noiseless case, we expect to measure .
Because of errors, we measure for a total of times.
We can thus estimate
Similarly, by running this other circuit,
we can estimate
Note: it is convenient to use a not-too-small as the statistical uncertainty scales as
(Bernoulli distribution) with .

## Slide 59: Simple example: 3. Post processing
We are now ready to run our desired circuit (using ) and measure the outcomes. We measure () a total of () times. It is convenient to organize the noisy result in a vector
, with .
Based on the characterization, we can construct a classical assignment matrix which relates the noisy output to the exact one :
We can thus invert the matrix to recover the exact results from the noisy one:
IF the simple model we used to describe readout noise is correct and IF the characterization is perfect, we are therefore able to “undo” the effect of the readout noise and recover the noiseless result (it’s a “bias-free” method)!

## Slide 60: Simple example: Sampling overhead
This very simple example is also extremely useful to highlight the sampling overhead associated with (generic) error mitigation strategies.
To this end, let’s focus on the statistical uncertainty (due to the finite number of shots) and assume, for simplicity, .
For the noisy result, the statistical uncertainty on simply read (Bernoulli distribution).
The mitigated result reads
The uncertainty on the mitigated result is thus amplified by the factor
To recover the statistical uncertainty of the noisy result, it is therefore needed to increase the number of shots by the square of the amplification factor.
NOTE: For a system where we measure qubits, the (exponential) overhead is .

## Slide 61: Simple example: Summary
We just saw an example of a readout error mitigation technique, which is noise-aware, bias-free and suffer from an overhead which is exponential in the error rate and in the number of qubits!
Note that, in practice, the sampling overhead of readout error mitigation is not a limiting factor. This is because, in many circuits of practical interest, the number of measurements (relevant to determine the observable or the probability distribution of interest) is much less than the number of gates. The exponential overhead of techniques that mitigate gate errors is therefore larger, typically.
In the following, we will see how to extend the simple example described so far to the multi-qubit case and how to use available tools to perform readout error mitigation in practice!

## Slide 62: Readout errors are not negligible
IQM Garnet
Zoom in to see actual values.
Confusion matrices indicate the error probabilities:
P(00¦00) | P(00¦01) | P(00¦10) | P(00¦11)
P(01¦00) | P(01¦01) | P(01¦10) | P(01¦11)
P(10¦00) | P(10¦01) | P(10¦10) | P(10¦11)
P(11¦00) | P(11¦01) | P(11¦10) | P(11¦11)
M =
P(Y|X) is the probability of observing state Y knowing that we prepared state X.

## Slide 63: Readout error mitigation
Calibration stage: Obtain confusion matrix M.
Run the quantum circuit in the noisy QPU and obtain .
Correction stage: find via the following equation:
[2] Yang, Bo, Rudy Raymond, and Shumpei Uno. "Efficient quantum readout-error mitigation for sparse measurement outcomes of near-term quantum devices." Physical Review A 106.1 (2022): 012423.
[1] Nation, Paul D., et al. "Scalable mitigation of measurement errors on quantum computers." PRX Quantum 2.4 (2021): 040326.

## Slide 64: Readout error mitigation
Calibration stage: Obtain confusion matrix M.
Let us assume that single-qubit readout errors dominate, then confusion matrix M reads,
P(0¦0) | P(0¦1)
P(1¦0) | P(1¦1)
=
=

## Slide 65: Readout error mitigation
Calibration stage: Obtain confusion matrix M.
Let us assume that single-qubit readout errors dominate, then confusion matrix M reads,
P(0¦0) | P(0¦1)
P(1¦0) | P(1¦1)
=
=
Many-qubit independent errors are still captured!
= x
e.g.

## Slide 66: Readout error mitigation
Calibration stage: Obtain confusion matrix M.
Let us assume that single-qubit readout errors dominate, then confusion matrix M reads,
P(0¦0) | P(0¦1)
P(1¦0) | P(1¦1)
=
=
How can we obtain all these matrices in a QPU?
“Marginal” method: 2 calibration circuits, where all qubits are either at state 0 or 1.
Independent method: 2n calibration circuits, where each qubit is independently prepared in state 0 or 1.
Balanced method: 2n calibration circuits, where each qubit state, 0 or 1 is prepared n times.

## Slide 67: Readout error mitigation
Calibration stage: Obtain confusion matrix M.
Run the quantum circuit in the noisy QPU and obtain .
Correction stage: find via the following equation:
(Non-twirling) techniques differ in the way they solve this equation
[2] Yang, Bo, Rudy Raymond, and Shumpei Uno. "Efficient quantum readout-error mitigation for sparse measurement outcomes of near-term quantum devices." Physical Review A 106.1 (2022): 012423.
[1] Nation, Paul D., et al. "Scalable mitigation of measurement errors on quantum computers." PRX Quantum 2.4 (2021): 040326.
With twirling
[3] Gupta, Riddhi S., et al. "Probabilistic error cancellation for dynamic quantum circuits." Physical Review A 109.6 (2024): 062617.
[4] Koh, Jin Ming, Dax Enshan Koh, and Jayne Thompson. "Readout error mitigation for mid-circuit measurements and feedforward." arXiv preprint arXiv:2406.07611 (2024).
[5] Hashim, Akel, et al. "Quasiprobabilistic Readout Correction of Midcircuit Measurements for Adaptive Feedback via Measurement Randomized Compiling." PRX Quantum 6.1 (2025): 010307.

## Slide 68: Readout error mitigation
Correction stage: find via the following equation:
NNLS is expensive and requires the construction of the 2n x 2n confusion matrix M. Therefore, techniques like M3 [1] or Bo et. al. [2], do not used constrained optimization.

## Slide 69: Readout error mitigation
Correction stage: find via the following equation:
NNLS is expensive and requires the construction of the 2n x 2n confusion matrix M. Therefore, techniques like M3 [1] or Bo et. al. [2], do not used constrained optimization.
They first reduce the confusion matrix dimensionality by assuming that limited by number of shots S.
M
Image source: Qiskit mthree package

## Slide 70: Readout error mitigation
Correction stage: find via the following equation:
NNLS is expensive and requires the construction of the 2n x 2n confusion matrix M. Therefore, techniques like M3 [1] or Bo et. al. [2], do not used constrained optimization.
They first reduce the confusion matrix dimensionality by assuming that limited by number of shots S.
LU factorization (direct) or iterative (matrix-free) methods available in open-source packages e.g. [1].
S<20000
O(S3) time
Buggy
(lower memory requirements and most likely faster; approximate variance calculation only)

## Slide 71: Readout error mitigation
Correction stage: find via the following equation:
NNLS is expensive and requires the construction of the 2n x 2n confusion matrix M. Therefore, techniques like M3 [1] or Bo et. al. [2], do not used constrained optimization.
They first reduce the confusion matrix dimensionality by assuming that limited by number of shots S.
LU factorization (direct) or iterative (matrix-free) methods available in open-source packages e.g. [1]
Bo et al. [2] can achieve it in O(nS2) time and memory scaling as O(S). Parallel computation is possible.

## Slide 72: Readout error mitigation
Correction stage: find via the following equation:
NNLS is expensive and requires the construction of the 2n x 2n confusion matrix M. Therefore, techniques like M3 [1] or Bo et. al. [2], do not used constrained optimization.
They first reduce the confusion matrix dimensionality by assuming that limited by number of shots S.
LU factorization (direct) or iterative (matrix-free) methods available in open-source packages e.g. [1].
Bo et al. [2] can achieve it in O(nS2) time and memory scaling as O(S). Parallel computation is possible.
[2]: Then (numerically) make the sum of the output vector elements be equal to 1 in O(S) time to get quasi-probability vector .

## Slide 73: Readout error mitigation
Correction stage: find via the following equation:
NNLS is expensive and requires the construction of the 2n x 2n confusion matrix M. Therefore, techniques like M3 [1] or Bo et. al. [2], do not used constrained optimization.
They first reduce the confusion matrix dimensionality by assuming that limited by number of shots S.
LU factorization (direct) or iterative (matrix-free) methods available in M3 [1].
Bo et al. [2] can achieve it in O(nS2) time and memory scaling as O(S). Parallel computation is possible.
[2]: Then (numerically) make the sum of the output vector elements be equal to 1 in O(S) time to get quasi-probability vector .
Lastly, find the nearest probability distribution from in O(S log(S)) time [1, 2].

## Slide 74: Readout error mitigation
Consider the following test:
Apply to all qubits in the Emerald QPU.
Obtain the average Z (or ZZ) observable outcome over all (nearest-neighbour) qubits and compute the mean absolute observable error, as follows,
.

## Slide 75: Readout error mitigation
Consider the following test:
Apply to all qubits in the Emerald QPU.
Obtain the average Z (or ZZ) observable outcome over all (nearest-neighbour) qubits and compute the mean absolute error.
24.03.2025
2Q (ZZ)
1Q (Z)

## Slide 76: Noise Robust Estimation (NRE) of Quantum Observables.
24.03.2025
arXiv:2503.06695
Noise-aware methods (PEC):
Requirement: Precise noise characterization.
Promise: Theoretically a bias-free estimation
Challenges: Pauli noise learnability, and parameter drifts
Finite bias in the final estimation
Noise-agnostic methods (ZNE, CDR, vnCDR, MDN):
Requirement: Noise-amplification, or training circuits, or both
Promise: Estimation of the noise-free observable (no guarantee)
Challenges: Various forms of model mismatch for different methods
Bias in the final estimation
Noise-Robust Estimation (NRE): Noise-agnostic and reliable
Using a novel correlation to address (and suppress) the ‘model mismatch’ problem.
Tested on IQM superconducting QPUs with circuits up to 20 qubits and 240 CZ gates.
Achieved highly accurate estimations, significantly outperforming other noise-agnostic methods.
PEC: Nature Physics 19, 1116 (2023)
ZNE: PRL 119, 180509 (2017)
CDR: Quantum 5, 592 (2021)
vnCDR: PRResearch 3, 033098 (2021)
MDN: Mitigating Depolarizing Noise on Quantum Computers with Noise-Estimation Circuits, PRL. 127, 270502 (2021)
Let’s take a closer look at ZNE first!

## Slide 77: Overview of Zero Noise Extrapolation (ZNE):
24.03.2025
Assume the noise of the system is characterized by a parameter
In practice, cannot be set to zero.
However, the noise can be amplified:
ZNE workflow:
Measure for different values of
Having a set of , extrapolate the data to the case where 0
Noise scale factor
Bias error
Challenge: | Example of model mismatch:
Knowing the precise scaling of by the noise scale factor | Assuming a certain mathematical function for (e.g. quadratic) which does not hold true.
Precise implementation of | Assuming certain values for that is different than the (unknown) truly implemented values.
Challenge: | Example of model mismatch:
 Bias error

## Slide 78
NRE Ansatz : An auxiliary quantity with reduced noise-sensitivity compared with
A key insight: Identification of a correlation between the unknown bias and a computable metric, normalized dispersion,
1st step post-processing: Baseline error-mitigated estimation (b-NRE) includes an unknown bias error,
Baseline
estimation
NRE framework
Notes: Let us start by giving a high-level overview on how NRE works. - the objective is of course to find the ideal expectation value of the observable of interest.
If we measure this observable, the outcome is noisy. Similar to ZNE, in this work, we parametrize the circuit error rate, and work with a dimensionless noise scale factor in the following slides.
NRE introduces an ansatz that is less sensitive to noise that directly measured expectation value.
Within the NRE framework, we have a first step post processing that gives us a baseline error mitigated value. This baseline estimation still contains bias error due to some model mismatch problems!
The key invention is that we discovered the bias is correlated with a calculable metric, normalized dispersion D.

## Slide 79
NRE Ansatz : An auxiliary quantity with reduced noise-sensitivity compared with
A key insight: Identification of a correlation between the unknown bias and a computable metric, normalized dispersion,
1st step post-processing: Baseline error-mitigated estimation (b-NRE) includes an unknown bias error,
2nd step post-processing: final NRE estimation with systematically reduced bias, using the correlation
Reduction of noise effect due to NRE
1st step
2nd step
Baseline
estimation
final
estimation
NRE framework
Notes: -this (correlation) enables us to set up the second post-processing step that systematically reduces the bias! And provides highly accurate
outcome! -let us now delve into more detail and introduce the NRE Ansatz

## Slide 80
NRE framework
Competition of noise effects!
(multi-)exponential with small exponent
Linear in
Linear in
Minimize noise-sensitivity
via tuning control parameter,
Control parameter, : A real-valued parameter used in the first-step post-processing
Noise-canceling circuit (): use to cancel the effect of the noise on
Structurally similar to the target circuit with known noiseless expectation value
We consider the “closest” Clifford circuit to the target circuit in the following results
Notes: -NRE Ansatz contains two parts.
In order to calculate these parts, in addition to executing a target circuit, we need to execute a noise-canclieng circuit!
This circuit is structurally similar to the target circuit, but with known noiseless expectation value
To Justify the form of the Ansatz, note that both part 1 and part 2 can be approximated by a linear function in \lambda! This enables the control-parameter introduced in the Ansatz to minimize noise-sensitivity of the Ansatz.

## Slide 81
NRE framework
and circuits are measured at values for the noise scale factor,
Taylor expansion:
: Bias error
The accuracy of the baseline estimation is limited by the unknown bias error.
The 2nd post-processing step aims to systematically reduce the bias error.
1st step post-processing:
baseline estimation:
Notes: Given that A(\lambda=0) is the ideal value we seek, we can write <O>_t in terms of Taylor expansion of A around lambda_1.
We then define the “optimal” control value as the one that renders the A(\lambda_1) and approximation of <O>_t = A(\lambda_1)
This then given the definition of the baseline estimation.
The accuracy of the baseline estimation is then determined by the unknown bias error!
We reduce the bias in the second post-processing step!

## Slide 82
NRE framework
Origin of the bias error :
Truncation
Discretization
Imprecise noise amplification
Higher-order
derivatives
Smaller variation in
across different values for
Smaller
Bias!
Normalized dispersion:
A proxy for bias
Bootstrapping a data set
2nd post-processing step:
MAD: Mean Absolute Deviation
Baseline estimation obtained from 2 bootstrap instances:
Notes: The origine of bias are : truncation, discretization and imprecise noise amplification.
The first two are given by higher order derivatives of A.
If A is a smother function of ‘lambda’ (i.e. smaller variation across different values for lambda) the higher order derivatives are expected to be smaller!
We define D as a metric that quantifies the smoothness of A, and therefore we anticipate that it can act as a proxy for bias.
Using bootstrapping, we generate a set of data showing the baseline estimation and their D values, and perform a data-regression method to find the value associated with D=0
The figure schematically shows the expectation values and the auxiliary quantity as a function of \lambda for two bootstrap instances. The right figure in there has smaller value for D, and as such, it is statistically more probable to give a more accurate estimation!

## Slide 83
NRE framework
Origin of the bias error :
Truncation
Discretization
Imprecise noise amplification
Higher-order
derivatives
Smaller variation in
across different values for
Smaller
Bias!
Normalized dispersion:
A proxy for bias
Bootstrapping a data set
2nd post-processing step:
MAD: Mean Absolute Deviation
Experimentally obtained baseline estimations
from 8 million bootstraps (shaded area):
Notes: The figure shows 8 million baseline estimations obtained by bootstrapping, and it makes it clear that B and D are correlated. The values associated with smaller D are having less bias (i.e. are more accurate). The red data point shows the final estimation using a linear regression.

## Slide 84
NRE verification I: ground state energy of Transverse-Field Ising Model (TFIM)
QPU: IQM Garnet
Qubit count: 20
CZ count: 240
Depth: 77
Observables of weight 1 and 2
Noise-amplification method:
Global unitary folding
Transverse field strength,
Target circuit is obtained by a QAOA ansatz with 4 layers
IQM Garnet is available on cloud:
https://resonance.meetiqm.com/
Notes: Example one: TFIM. Qubit count: 20, CZ count: 240, Depth: 77, Observables of weight 1 and 2
At the lowest value for lambda, the <o> is reduces from the noise-less value by around 40%

## Slide 85
NRE verification I: ground state energy of Transverse-Field Ising Model (TFIM)
NRE: Averaged over 200 bootstrap sets # of baseline estimations per single
bootstrap index =
Total number of shots:
NRE:
Highly-accurate and stable predictions
Persistently outperforming other methods
Transverse field strength,
Target circuit is obtained by a QAOA ansatz with 4 layers
Notes: - Upper panels show the correlation between the bias of the baseline estimations and the normalized dispersion. Different panels are obtained by having different settings for the noise scale factor.
- NRE successfully recovers the expectation value with high accuracy for all different settings for noise amplification.
- NRE outperforms other methods in reducing the error (lower panels) by UP to two-orders of magnitude (in panel i)

## Slide 86: Conclusion

## Slide 87: Conclusion
Quantum computing holds big promise, but noise remains a fundamental challenge. In these slides, we explored:
Noise Processes – We discussed coherent errors (e.g., unitary over-rotations) and modelled incoherent (e.g., T₁/T₂ processes) errors, showing how they affect gate operations and idle qubits. Understanding these processes is crucial for developing effective error reduction techniques (error suppression and mitigation).
Error Suppression – Techniques like dynamical decoupling (to mitigate coherent errors and non-Markovian errors, for example) and Pauli twirling (to convert coherent noise into stochastic noise channels) help reduce errors in quantum circuits before they accumulate.
Error Mitigation – Methods such as readout error mitigation (correcting measurement inaccuracies) and Noise Robust Estimation (NRE) further improve results in the presence of unavoidable noise.